## Slide 1
MICROPROCESSOR AND COMPUTER ARCHITECTURE LABORATORY
4TH Semester(UE19CS256)
Prof Deepti C
Computer Science and Engineering
Class 3 Week2
Tuesday, February 2, 2021

## Slide 2
Microprocessor & Computer Architecture Laboratory
WEEK 2 | 1.Based on the value of the number in R0, Write an ALP to store 1 in R1 if R0 is zero, Store 2 in R1 if R0 is positive, Store 3 in R1 if R0 is negative. ( Program shown in class) 2.Write an ALP to compare the value of R0 and R1, add if R0 = R1, else subtract ( Program shown in class) 3.Write an ALP to find the factorial of a number stored in R0. Store the value in R1 (without using LDR and STR instructions).Use only registers. ( Program shown in class) 4.a)Write an ALP to add two 32 bit numbers loaded from memory and store the result in memory. b)Write an ALP to add two 16 bit numbers loaded from memory and store the result in memory.

## Slide 3
Microprocessor & Computer Architecture Laboratory
WEEK 2 | 5. a)Write an ALP to find GCD of two numbers (without using LDR and STR instructions).Both numbers are in registers. Use only registers. b)Write an ALP to find the GCD of given numbers (both numbers in memory).Store result in memory. 6.a) Write an ALP to add an array of ten 32 bit numbers from memory. b) Write an ALP to add array of ten 8 bit numbers taking data from memory location stored as byte data (use .byte to store the data instead of .word) 7. Write an ALP to multiply 35*R0 *Use LSL instruction for multiplication 8.Write an ALP to evaluate the expression (A+B)+(3*B) a)using LSL instruction(use registers) b) Using MUL instruction

## Slide 4
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 1
WEEK 2 | Based on the value of the number in R0, Write an ALP to store 1 in R1 if R0 is zero, Store 2 in R1 if R0 is positive, Store 3 in R1 if R0 is negative. ( Program shown in class)
CASE 1 | R0 |  | 0x00
 | R1 | After compare | 1
CASE 2 | R0 |  | 0x05
 | R1 | After compare | 2
CASE 3 | R0 |  | 0xFF
 | R1 | After compare | 3
Algorithm
1.The number is to be saved in R0
2.Compare the given number with zero
3.If the given number is zero,R1=1, end execution
4.If the given number is negative,R1=3, end execution
5.If the given number is neither zero nor negative,the number is assumed to be positive,R1=2,end execution.
(Three Screenshots-Choose your own example to cover all three cases)

## Slide 5
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 2
WEEK 2 | Write an ALP to compare the value of R0 and R1, add if R0 = R1, else subtract ( Program shown in class)
CASE 1 | R1=0x05, R0=0x05 R2=R1+R0=0x0A |  | 
CASE 2 | R1=0x06,R0=0x05 R2=R1-R0=0x01 |  | 
Algorithm
1.The first number is to be saved in R0
2.The second number is to be saved in R1
3.Compare the two numbers
4.If they are equal,branch to location L1 where both numbers are added.
5.Save the addition result in R2 and end execution
6.If the numbers are not equal subtract the two numbers.
7.Save subtraction result in R2 and end execution.
(Two Screenshots-Choose your own example to cover all two cases)

## Slide 6
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 3
WEEK 2 | Write an ALP to find the factorial of a number stored in R0. Store the value in R1 (without using LDR and STR instructions).Use only registers.( Program shown in class)
1st Iteration | R1=0x05 R0=0x04 R2=0X14=Decimal 20
2nd Iteration | R1=0x14 R0=0X03R2=0x3C=Decimal 60
3rd Iteration | R1=0x3C R0=0X02R2=0x78
4th Iteration | R1=0x78 R0=0X01R2=0x78 =Decimal 120
Algorithm
1.The number n is to be saved in R0
2.Copy the same number to R1
3.Subtract the contents of R0 by 1 to calculate n-1
4.Multiply n *(n-1) i.e,the contents of R1 and R0
5.Save multiplication result in R2.
6.Copy the multiplication result to R1
7.Check if the content of R0 is one
8.Repeat steps 3 to 7 till R0 reaches one
9.End execution when R0=1
(One Screenshot-Choose your own example)

## Slide 7
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 4a)
WEEK 2 | Write an ALP to add two 32 bit numbers loaded from memory and store the result in memory.
 | A=0x0A, B=0x14
R0 | Address of A
R1 | Address of B
R2 | Address of C
R3 | 0x14=Decimal 20 =Content of Location B
R4 | 0x0A=Decimal 10= Content of Location A
R5 | 0x1E=Decimal 30
Location C | 0x1E=Decimal 30
Algorithm
1.Let R0 =>contain the address of the first number (location A)
2.Let R1 =>contain the address of the second number(location B)
3.Let R2 =>contain the address of location C where addition result is to be finally stored.
4.Copy the second number to R3
5.Copy the first number to R4
6.Add both the numbers in R3 and R4
7.Save the addition result in R5
8.Store the result in R5 in memory location C
(One Screenshot-Choose your own example)

## Slide 8
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 4b)
WEEK 2 | Write an ALP to add two 16 bit numbers loaded from memory and store the result in memory.
 | A=0x0A, B=0x14
R0 | Address of A
R1 | Address of B
R2 | Address of C
R3 | 0x14=Decimal 20=Content of Location B
R4 | 0x0A=Decimal 10= Content of Location A
R5 | 0x1E=Decimal 30
Location C | 0x1E=Decimal 30
Algorithm
1.Let R0 =>contain the address of the first number (location A)
2.Let R1 =>contain the address of the second number(location B)
3.Let R2 =>contain the address of location C where addition result is to be finally stored.
4.Copy the second number to R3
5.Copy the first number to R4
6.Add both the numbers in R3 and R4
7.Save the addition result in R5
8.Store the result in R5 in memory location C
Note :Use instructions ldrh,strh,.hword
(One Screenshot-Choose your own example)

## Slide 9
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 5a)
WEEK 2 | Write an ALP to find GCD of two numbers (without using LDR and STR instructions).Both numbers are in registers. Use only registers.
CASE 1 | R0 | 0x0A
 | R1 | 0x0F
1st iteration | R2=0x0A R3=0x0F R3=0x0F-0x0A=0x05 | 
2nd iteration | R2=0x0A R3=0x05 R2=0x0A-0x05=0x05 | 
3rd iteration | R2=0x05 R3=0x05 GCD=5 | 
Algorithm
1.The first number is to be saved in R0
2.The second number is to be saved in R1
3.Copy the first number to R2
4.Copy the second number to R3.
5.Compare both numbers in R2 and R3.
6.If they are equal, end execution
7.If R2 is less than R3,R3= R3-R2
8.Repeat steps 5 to 7 till R2=R3, end execution
9.If R2 is greater than R3,R2= R2-R3
10. Repeat steps 5 to 7 till R2=R3, end execution
(Three Screenshots(A=B,A<B,A>B) Choose your own example)

## Slide 10
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 5b)
WEEK 2 | Write an ALP to find the GCD of given numbers (both numbers in memory).Store result in memory.
CASE 1 | A=0x14,B=0x04
1st iteration | R2=0x14=Decimal 20 R3=0x04 R2=0x14-0x04=0x10
2nd iteration | R2=0x10=Decimal 16 R3=0x04 R2=0x10-0x04=0x0C
3rd iteration | R2=0x0C=Decimal 12 R3=0x04 R2=0x0C-0x04=0x08
4th iteration | R2=0x08 R3=0x04 R2=0x08-0x04=0x04
5th iteration | R2=0x04 R3=0x04
Algorithm
1.R0 => address of A
2.R1 => address of B
3.Copy the value of A to register r2
4.Copy the value of B to register r3
4.Compare A and B values in Register R2 and R3 respectively
5.If both are equal end execution
6.If A is lesser than B,R3=R3-R2
7.Repeat Steps 4 to 6 till R2 is equal to R3 and end execution.
8.If A is greater than B,R2=R2-R3
9.Repeat steps 4 to 6 till R2 is equal to R3
and end execution.
(Three Screenshots(A=B,A<B,A>B)
-Choose your own example)

## Slide 11
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 6a)
WEEK 2 | Write an ALP to add an array of ten 32 bit numbers from memory
A:.word 10,20,30,40,50,60,70,80,90,11 |  |  |  |  |  |  |  |  |  | 
R1 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
R0 | A | A+4 | A+8 | A+ 12 | A+16 | A+20 | A+ 24 | A+28 | A+32 | A+36
R2 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 11
R3 | 0 | 10 | 30 | 60 | 100 | 150 | 210 | 280 | 360 | 450
R3 (After Execution) | 10 | 30 | 60 | 100 | 150 | 210 | 280 | 360 | 450 | 461
Values in hex | 0x0A | 0x 1E | 0x 4C | 0x 64 | 0x 96 | 0x D2 | 0x 118 | 0x 168 | 0x 1C2 | 0x 1CD
Algorithm
1.Let R0 contain the address of the first number in array A
2.Let R1 contain the count =total numbers in the array=10
3.Let R3=Initial sum value=0
4.Copy the first number in the array to R2
5.Increment R0 to point to the next word(R0=R0+4)
6.Add both the numbers in R3 and R2
7.Save the addition result in R3
8.Decrement the count in r1
9.Repeat steps 4 to 8 till r1=0
10.If r1=0 end execution
(One Screenshot-Choose your own example)

## Slide 12
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 6b)
WEEK 2 | Write an ALP to add an array of five 8 bit numbers from memory(use .byte to store the data instead of .word)
A:.byte 1,2,3,4,5 |  |  |  |  | 
R1 | 5 | 4 | 3 | 2 | 1
R0 | A | A+1 | A+2 | A+3 | A+4
R3 | 0 | 1 | 3 | 6 | 10
R4 | 1 | 2 | 3 | 4 | 5
R3 (After Execution) | 1 | 3 | 6 | 10 | 15
Values in hex | 0x 01 | 0x 03 | 0x 06 | 0x 0A | 0x 0F
Algorithm
1.Let R0 contain the address of the first number in array A
2.Let R1 contain the count =total number of values in the array=5
3.Let R3=Initial sum value=0
4.Copy the first number in the array to R2
5.Increment R0 to point to the next byte(R0=R0+1)
6.Add both the numbers in R3 and R2
7.Save the addition result in R3
8.Decrement the count in r1 by 1
9.Repeat steps 4 to 8 till r1=0
10.If r1=0 end execution
(One Screenshot-Choose your own example)

## Slide 13
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 7
WEEK 2 | Write an ALP to multiply 35*R0 *Use LSL instruction for multiplication
 | Decimal | Hexadecimal
R0(1st line of the Program) | 50 | 32
R0(2nd line of the Program | 4R0=200 | C8
 | 4R0+R0= 5R0=250 | FA
R0(3rd line of the Program | 8R0=250*8=2000 | 0x7D0
 | 8R0-R0=1750 | 6D6
Algorithm
1.The first number to be saved in R0(say R0=Decimal 50)
2.To Multiply R0 value with 5 .
Implement R0=(4*R0)+R0
Hint:Use LSL Instruction to multiply by 4
3.To multiply the obtained value of R0 by 7
Implement R0=(8*R0)-R0=7R0
Hint:Use LSL Instruction to multiply by 8
4.End program
One Screenshot-Choose your own value for R0

## Slide 14
Microprocessor & Computer Architecture Laboratory
 | PROGRAM 8
WEEK 2 | Write an ALP to evaluate the expression (A+B) + (5*B), where A and B are available in memory location. 9.Store the final result in memory Location C * Use LSL instruction for multiplication
A=Decimal 50,B=Decimal 19 |  | 
 | Decimal | Hexadecimal
R3 R4 | 50 19 | 32 13
R5 =R3+R4 =A+B | 69 | 45
Calculate 4*B | 19*4=76 | 4C
Calculate 5*B | 76+19=95 | 5F
Calculate (A+B)+5*B | 69+95=164 | A4
Algorithm
1.R0 => address of A
2.R1 => address of B
3. R2 => address of C
4.Copy the value at Location A into R3
5. Copy the value at Location B into R4
6.Calculate A+B
7.Calculate 4*B (use LSL instruction)
. Calculate 5*B
8. Calculate (A+B)+5*B
9.Store the final result in memory Location C
(One Screenshot-Choose your own value for A and B)

## Slide 15
deeptic@pes.edu
THANK YOU
Deepti C
Department of Computer Science and Engineering