## Slide 1
MICROPROCESSOR AND COMPUTER ARCHITECTURE LABORATORY
4TH Semester(UE19CS256)
Prof Deepti C
Computer Science and Engineering
Class 7 Week6
Saturday, February 27, 2021

## Slide 2
Microprocessor & Computer Architecture Laboratory
 | ARMSIM EMBEST BOARD PLUGIN PROGRAMS
WEEK 6 | 1.Write an ALP to blink LEDs. First, the right LED is switched on and the left LED is switched off. After 1 second, the right LED is switched off and the left LED is switched on and the program continue to blink both the LEDs. 2. Write an ALP to display 0-9,A-F(up and down count) on an 8 segment display 3. Write an ALP to move a string from Right to Left on LCD (40 columns by 15 rows).

## Slide 3: SWI Operations for EMBEST BOARD Plug‐Ins:
The SWI codes numbered greater than 255 have special purposes.
They are mainly used for interaction with Plug‐in modules which can be loaded with the ARMSim# simulator.
The use of “EQU” is strongly advised to substitute the actual numerical code values. Examples of code is also provided at the end of the section.
The default installation of ARMSim# comes with two Plug‐ins module extensions: SWIInstructions and EmbestBoard.
Important Note: All Plug‐ins have to be enabled explicitly by checking their option in the File > Preferences menu and selecting the appropriate line from within the tab labelled Plugins.

## Slide 4: To run the codes,
Install ARMSIM simulator
Go to File-->Preferences->Plugins and select "Embest Board Plugin"
Go to view-->PluginsUI
Run the code(File Load-Select the program written in notepad file with extension .s

## Slide 5
There are 5 main components in this view available for programming:
One 8‐segment display (output).
Two red LED lights (output).
Two black buttons (input).
Sixteen blue buttons arranged in a keyboard 4 x 4 grid (input).
One LCD display screen, which is a grid of 40 columns by 15 rows of individual cells. The coordinates for each LCD cell are specified by a {column, row} pair. The top‐left cell has coordinates {0,0},while the bottom‐right cell has coordinates {39,14}. Each cell can contain exactly one ASCII character.
EMBEST BOARD View

## Slide 7
SWI #
Opcode | Description | Inputs | Outputs
swi 0x200 | Light up the 8 segment display | r0: the 8‐segment Pattern | The appropriate segments light up to display a number or a character
swi 0x201 | Light up the two LEDs | r0: the LED Pattern, where: Left LED on = 0x02 Right LED on = 0x01 Both LEDs on = 0x03 (i.e. the bits in position 0 and 1 of r0 must each be set to 1 appropriately) | Either the left LED is on, or the right, or both
swi 0x202 | Check if one of the Black Buttons has been pressed. | None | r0 = the Black Button Pattern, where: Left black button pressed returns r0 = 0x02; Right black button pressed returns r0 = 0x01; (i.e. the bits in position 0 and 1 of r0 get assigned the appropriate values).

## Slide 8
SWI #
Opcode | Description | Inputs | Outputs
swi 0x204 | Display string on LCD at row, column position | r0: x position coordinate on the LCD screen (0‐39); r1: y position coordinate on the LCD screen (0‐14); r2: Address of a null terminated ASCII string. Note: (x,y) = (0,0) is the top left and (0,14) is the bot‐ tom left. The display is limited to 40 characters per line | The string is displayed starting at the given position of the LCD screen
swi 0x206 | Clear the display on the LCD screen | None | Blank LCD screen
swi 0x207 | Display a character on the LCD screen | r0: x position coordinate on the LCD screen (0‐39); r1: y position coordinate on the LCD screen (0‐14); r2: the character. Note: (x,y) = (0,0) is the top left and (0,14) is the bot‐ tom left. The display is limited to 40 characters per line | The string is displayed starting at the given position of the LCD screen.
swi 0x208 | Clear one line in the dis‐ play on the LCD screen | r0: line number (y coordi‐ nate) on the LCD screen | Blank line on the LCD screen.

## Slide 9
SWI Codes used in PROGRAM 1
Set the LED to light up: LED Light Up.s

## Slide 10
Microprocessor & Computer Architecture Laboratory
WEEK 6 | PROGRAM 1 | 
Write an ALP to set the LED to light up |  | 
Algorithm 1.Initially let R0=0 2.Use SWI 0x201 to configure LEDs to light up(To light up LED ,r0= 1 means right led light up,r0=2 means left LED and r0=3 means both LED light up) 3. Increment r0 by 1 4.To introduce delay between the three LED options, Initialize one delay register with a large value for example 64000 5.a)Begin delay procedure by decrementing delay register by 1 b)Check if delay register is equal to zero c)Repeat Step 5 and 6 till delay register reaches zero 6.Compare r0 value with 3(Check if all the three options have been displayed) 7.Repeat steps 2 to 6 till r0 is less than or equal to 3. 8.End Program |  | 

## Slide 11
PROGRAM 2
Set the 8‐Segment Display to light up: Eight Segment .s

## Slide 12
The “.equ” statements are useful for accessing the byte values associated with the labels of each segment as shown in Figure.
The byte values representing a particular number are already “ORed” together within the array data structure and can be indexed appropriately.
It may be easier to use a data declaration for an array of words and then index into it. Each element can be initialized to contain the value representing a number by having the appropriate byte values “ORed” together.

## Slide 14
0 | Segment A+ Segment B +Segment C +Segment D +Segment E + Segment G | 0x80+0x40+0x20+0x08+0x04+0x01 =0b11101101=0xED
1 | Segment B +Segment C | 0x40+0x20=0b01100000=0x60
2 | Segment A+ Segment B + Segment D+ Segment E Segment F | 0x80+0x40+0x08+0x04+0x02 =0b11001110=0xCE
3 | Segment A+ Segment B +Segment C +Segment D + Segment F | 0x80+0x40+0x20+0x08+0x10+0x02 =0b11111010=0xFA
4 | Segment B +Segment C+ Segment F + Segment G | 0x40+0x20+0x02+0x01 =0b01100011=0x63
5 | Segment A +Segment C +Segment D +Segment F + Segment G | 0x80+0x20+0x08++0x02+0x01 =0b10101011=0xAB
6 | Segment A +Segment C +Segment D +Segment E + Segment F +Segment G | 0x80+0x20+0x08+0x04+0x02+0x01 =0b10101101=0xAF
7 | Segment A+ Segment B +Segment C | 0x80+0x40+0x20==0b11100000=0xE0
8 | Segment A+ Segment B +Segment C +Segment D +Segment E + Segment F+ Segment G | 0x80+0x40+0x20+0x08+0x04++0x02 +0x01=0b11101101=0xEF
9 | Segment A+ Segment B +Segment C Segment F+ Segment G | 0x80+0x40+0x20+0x02+0x01 =0b11100011=0xE3

## Slide 15
A | Segment A+ Segment B+ Segment C+ Segment E + Segment F+ Segment G | 0x80+0x40+0x20+0x04+0x02+0x01 0b11100111=0xE7
B | Segment C+ Segment D+ Segment E + Segment F+ Segment G | 0x20+0x08+0x04+0x02+0x01 0b00101111=0x2F
C | Segment A+ Segment D+ Segment E + Segment G | 0x80+0x08+0x04+0x01 =0b10001101=0x8D
D | Segment B +Segment C+ Segment D+ Segment E+ Segment F + Segment G | 0x40+0x20+0x04+0x08+0x02 =0b01101110=0x6E
E | Segment A+ Segment D +Segment E + Segment F+ Segment G | 0x80+0x08+0x04+0x02+0x01 0b10001111=0x8F
F | Segment A+ Segment E + Segment F+ Segment G | 0x80+0x04+0x02+0x01 0b10000111=0x87

## Slide 16
Microprocessor & Computer Architecture Laboratory
WEEK 6 | PROGRAM 2 | 
Write an ALP to display 0 to F and F-0 on the 8 segment display depending on the which black button is pressed: |  | 
Algorithm Initially let R0=0, R2=0 Procedure again: 2.a)Begin by using SWI 0x202 to check whether black button pressed or not b)Check if r0=1,branch to loop1 for count in ascending order c) Check if r0=2,branch to loop2 for count in descending order 3.Repeat steps 2a,2b,2c 4.Begin loop1 by loading r5 with 16 5.Let r1 point to the first seven segment display code i.e zero |  | 

## Slide 17
Microprocessor & Computer Architecture Laboratory
WEEK 6 | PROGRAM 2 | 
6.back1:a)Copy each value from data segment byte wise to r0 b).Use swi 0x200 ; Set 8 segment display to light up c)Include branch to delay procedure d)Increment r1 by 1(Go to next number) e)Decrement r5 by 1(Decrement total count) f)Compare r5 with zero g)Repeat steps 6a to 6f till r5 not equal to zero 7.Repeat steps 2 to 6f (Procedure again) 8. a)Begin loop2 by loading r5 with 6 b)Let r1 point to the seven segment display code of F c)Copy each value from data segment byte wise to r0 d).Use swi 0x200 ; Set 8 segment display to light up |  | 

## Slide 18
Microprocessor & Computer Architecture Laboratory
WEEK 6 | PROGRAM 2 | 
6.back1:a)Copy each value from data segment byte wise to r0 b).Use swi 0x200 ; Set 8 segment display to light up c)Include branch to delay procedure d)Increment r1 by 1(Go to next number) e)Decrement r5 by 1(Decrement total count after each number) f)Compare r5 with zero g)Repeat steps 6a to 6f till r5 not equal to zero 7.Repeat steps 2 to 6f (Procedure again) 8. a)Begin loop2 by loading r5 with 6 b)Let r1 point to the seven segment display code of F c)Copy each value from data segment byte wise to r0 d).Use swi 0x200 ; Set 8 segment display to light up e)Branch to delay procedure |  | 

## Slide 19
Microprocessor & Computer Architecture Laboratory
WEEK 6 | PROGRAM 2 | 
f)Decrement r1 by 1 g)Decrement r5 by 1 h)Compare r5 with zero i)Repeat steps 8c to 8h till r5 not equal to zero h)Repeat steps 2 to 8h (Procedure again) Delay Procedure a)Let r4 contain a large value like 64000 b)Decrement r4 by 1 c)Check if r4 has reached zero d)Decrement till r4 ==0 e)Return to main program |  | 

## Slide 20
PROGRAM 3 Move a string left to right ,right to left on LCD in Embest Board

## Slide 21
.data
str: .asciz "HELLO WORLD"
num: .word 15000
Algorithm
1.Let r0 contain the x coordinate position
2.Let r1 contain the y coordinate position
3. Let r2 point to the string that has to be displayed
4.Let r8 point to the delay value num in data segment
5.Copy value num from memory to a register r6
6.Initialise r7=0
7.Use swi0x204 to initialize string display
8.a)Branch to delay procedure, Increment count in r7 by 1
b)Compare r7 with num
c)Continue to increment r7 till it reaches num value
PROGRAM 3 Move a string left to right ,right to left on LCD in Embest Board

## Slide 22
d)Clear one line in the LCD display using SWI 0x206
e)Load r7 with zero again
f)Return to main program( mov pc, lr)
9.Compare r0(rows count) with zero
10.Decrement r0 by 1 until r0 reaches zero
11.If r0=0 terminate else repeat steps 7 to 10
PROGRAM 3 Move a string left to right ,right to left on LCD in Embest Board